## Slide 1: Positional Number Systems
COSC 102
Camille Crumpton

## Slide 2: Topics
Decimal
Binary
Hexadecimal
Converting

## Slide 3: What is a Positional Number System?
A way to represent a number and its magnitude using the “position” a digit is placed
Base determines the power base
  Decimal 10p
  Binary 2p
  Hexadecimal 16p
  Octal 8p
Place starts with power 0 (just like array index)
Base has digits 0 – (base – 1)
  Decimal 0 – 9
  Binary 0 – 1
  Hexadecimal 0 – F
  Octal 0 - 7

## Slide 4: Decimal (Base 10)
The weight of each digit of a decimal number depends on its relative position within the number
ex. One thousand, two hundred twenty-four
1s Place
10s Place
100s Place
1000s Place
1
2
3
4

## Slide 5: Decimal (Base 10)
Decimal
  1234:
    1(1000) + 2(100) + 3(10) + 4(1)
  Decimal consists of powers of 10
    1000 (103), 100 (102), 10 (101), 1 (100)
  For each ascending place, its magnitude grows 10x
  1 2 3 4
1s Place
10s Place
100s Place
1000s Place

## Slide 6: Fractions (Base 10)
Descending place, its magnitude is divided by 10
27.212
  2(10) + 7(1) + 2(10-1) + 1(10-2) + 2(10-3)
  2(10) + 7(1) + 2(.1) + 1(.01) + 2(.001)
10ths Place
100ths Place
1000ths Place

## Slide 7: Binary (Base 2)
A digit in binary (0 or 1) is also called a bit. Only these two digits are used in binary.
Like a decimal number, the weight of each binary bit of a binary number depends on its relative position within the number
  For each ascending place, its magnitude grows 2x

## Slide 8: Binary (Base 2)
Binary (base 2)
  1101
    1(8) + 1(4) + 0(2) + 1(1)
  Binary consists of powers of 2
    8 (23), 4 (22), 2 (21), 1 (20)
  For each ascending place, its magnitude grows 2x
  1 1 0 1
1s Place
2s Place
4s Place
8s Place

## Slide 9: Distinguishing Base 2
Is 1101
  One thousand, one hundred, one?
    1(1000) + 1(100) + 0(10) + 1(1)
  Thirteen?
    1(8) + 1(4) + 0(2) + 1(1)
Distinguish from base 10 by prefix or suffix
  0b1101 = Binary 1101 (0b means binary)
    This is how you represent binary in C++ and assembly
  11012 = Binary 1101 (subscript 2 means binary)

## Slide 10: Fractions (Base 2)
Descending place, its magnitude is divided by 2
10.1102 = 2.7510
  1(2) + 0(1) + 1(2-1) + 1(2-2) + 0(2-3)
  1(2) + 0(1) + 1(.5) + 1(.25) + 0(.125)
1/2ths Place
1/4ths Place
1/8ths Place

## Slide 11: Why Binary?
Binary represents on (1) or off (0), true or false, yes or no.
  1 = voltage on (typically)
  0 = voltage off
Computers use a group of 8 binary digits (bits), which is called a “byte”.
  0b0101_0011 = 1 byte

## Slide 12: Hexadecimal Digits
Hexadecimal number system has a base of 16… so how do we represent any digit bigger than 9? 10 can’t work for ten – it’s two digits, and we need a single digit.
Digits > 9 are represented by a letter A-F
  A = 10
  B = 11
  C = 12
  D = 13
  E = 14
  F = 15
NOTE: Case does not typically matter and in programming, we use lower-case letters.

## Slide 13: Hexadecimal (Base 16)
Hexadecimal
  19AC
    1(4096) + 9(256) + A(16) + C(1)
  Hexadecimal consists of powers of 16
    4096 (163), 256 (162), 16 (161), 1 (160)
  For each place, its magnitude grows 16x
  1 9 A C
1s Place
16s Place
256s Place
4096s Place

## Slide 14: Distinguishing Base 16
Is 16
  Sixteen? 1(10) + 6(1)
  Twenty-two? 1(16) + 6(1)
Distinguish from base 10 by prefix or suffix
  0x16 = Hex 16 (0x means hex)
    This is how you represent hex in C++ and assembly
  1616 = Hex 16 (subscript 16 means hex)

## Slide 15: Fractions (Base 16)
Descending place, its magnitude is divided by 16
2E.1AA16 = 46.1040039062510
  2(16) + E(1) + 1(.0625) + A(.00390625) + A(.000244140625)
1/16ths Place
1/4096ths Place
1/256ths Place

## Slide 16: Number System Comparison

## Slide 17: Number System Comparison

## Slide 18: Practice
Magnitude of
  0xA5
    A(16) + 5(1)
      10(16) + 5 = 160 + 5 = 165
  0x1C
    1(16) + C(1)
      16 + 12 = 28
  0b0001_1001
    1(16) + 1(8) + 0(4) + 0(2) + 1(1)
      16 + 8 + 1 = 24 + 1 = 25
  0b0000_1111
    1(8) + 1(4) + 1(2) + 1(1)
      8 + 4 + 2 + 1 = 15

## Slide 19: Practice
Magnitude of
  0xA.2
    A(1) + 2(1/16)
      10(1) + 2/16 = 10 + 1/8 = 10 + 0.125 = 10.125
  0x1.0A
    1(1) + 0(1/16) + A(1/256)
      1 + 10/256 = 1.0390625
  0b11.011
    1(2) + 1(1) + 0(1/2) + 1(1/4) + 1(1/8)
      2 + 1 + 0.25 + 0.125 = 3 + 0.375 = 3.375
  0b1.1111
    1(1) + 1(1/2) + 1(1/4) + 1(1/8) + 1(1/16)
      1 + 0.5 + 0.25 + 0.125 + 0.0625
        1.75 + 0.1875 = 1.9375

## Slide 20: Converting To Base 2
84
  Need to find powers of two that add up to 84
Find largest power of 2 that comes closest to 84, but not over. Your first 1 will go here. Subtract 84 by the power, repeat.
  27 = 128 (too large)
  26 = 64 (closest to 84) Index 6 gets 1
    84 – 64 = 20 (still need to represent 20)
  25 = 32 (bigger than 20) Index 5 gets 0
  24 = 16 (closest to 20) Index 4 gets 1
    20 – 16 = 4 (still need to represent 4)
  23 = 8 (too large) Index 3 gets 0
  22 = 4 (closest to 4) Index 2 gets 1
    4 – 4 = 0
  21 = 2 (too large) Index 1 gets 0
  20 = 1 (too large) Index 0 gets 0

## Slide 21: Fraction Converting Base 2
0.6875
  Start with 2-1 then move to 2-2 and if the magnitude is <= the value, put a 1, otherwise put a 0.
  2-1 = 0.5 1 (.1875 remaining)
  2-2 = 0.25 0 (too big)
  2-3 = 0.125 1 (.0625 remaining)
  2-4 = 0.0625 1 (0 remaining)
0.687510 = 0.10112

## Slide 22: Easy Converting To Base 16
124
  First, convert to binary
    0b0111_1100
Each 1 hex digit is 4 binary digits
  Take groups of four at a time
    0111 = 7 = 0x7
    1100 = 12 = 0xc
    0x7c

## Slide 23: Fraction Converting Base 16
Same way!
0x3.A4
  0b0011.1010_0100
    1(2) + 1(1) + 1(1/2) + 1(1/8) + 1(1/64)
      3.(0.5 + 0.125 + 0.015625)
      3.640625

## Slide 24: Topics
Decimal
Binary
Hexadecimal
Converting

## Slide 25: Number Systems COSC 102 Camille Crumpton